## Slide 1: Low-Variance Retrial Times in a Multiserver Queueing Model
Prof. Andrew Ross, David Lubke,
Andrew Livingston, Katherine Ballentine
Eastern Michigan University,
Ypsilanti, Michigan
CanQueue 2009, Univ. of Windsor

## Slide 2
ORBIT
Servers
Arrive
Depart
If all servers are busy, incoming or retrying calls are bounced to orbit
Calls retry to enter service

## Slide 3: Multiserver Retrial Queues
Mobile phone: link to tower
Satellite phone/data: link to satellite
Dial-up internet
Credit card verification
All have non-exponential retrials
Notes: Mobile Phone and Sat. Phone might be more variable than exponential,
Dial-up and credit-card verification would be less variable than exponential, nearly deterministic.
Mobile phone: 56 channels/cell for old analog technology (FDMA, 1G),
3 times that (168) for TDMA 2G,
8-10 times FDMA for CDMA 2G

## Slide 4
Number in Orbit
Number in Service
Total Number in System
Time
Number of Jobs
Retrial rate = 1 per hour = service rate
Notes: Here is a sample path of a simulated system. 12 servers (note the green curve tops out at 12).
We often have people in orbit even though some servers are free (point to examples).

## Slide 5: Single-Server Systems: Distribution matters!
Ethernet and WiFi deliberately avoid using deterministic retrial distributions
They are single-server systems, though
Multi-server systems generally act differently for measures like probability of delay.

## Slide 6: Our Main Question
When must you take the retrial distribution into account?
Methods:
  Discrete-event simulation
  Markov-chain computation
Notes: Ross will present the simulation results,
Livingston and Ballentine will present the Markov results.
Our focus is not on computation methods, but on numeric results.

## Slide 7: M/M/c/0 + G-retrials
Poisson arrivals with constant rate
Exponential service
No organized buffer
Everyone in orbit retries
  not just one person
Customers never give up
Notes: Why exponential service? We looked at non-exponential service earlier, and the results were not as interesting
Why no buffer? Buffer interpolates between Retrial and Ordinary queue; we want to study retrials.
Why perfect persistence? Imperfect persistence interpolates between Retrial and Loss system; we want to study retrials.

## Slide 8: Square-Root Staffing
Servers = traffic + 1*sqrt(traffic)
QED: Quality and Efficiency Domain
Notes: Medium traffic, neither heavy-traffic nor light-traffic
Quality-and-Efficiency Domain (QED), not QD (servers=1.1*traffic) or ED (servers=traffic + 10)
Another name for QED is the Halfin-Whitt regime

## Slide 9: Lo as system grows
0
5
10
15
20
0
20
40
60
80
100
120
sqrt(traffic)
Lo
0.1
1
10
100
1000
Retrial rate
Notes: Very nearly linear in sqrt(traffic), just like Erlang-C systems
Circles at the bottom are the Erlang-C Lq values

## Slide 10: Wo as system grows
0
10
20
0
1
2
3
4
5
sqrt(traffic)
Wo
0.1
1
10
100
1000
Notes: Wo decays as 1/sqrt(traffic), just like Erlang-C
Circles at the bottom are Erlang-C Wq values

## Slide 11: Pr(new arrival delayed)
0
5
10
15
20
0
0.05
0.1
0.15
0.2
0.25
0.3
0.35
sqrt(traffic)
Pr(new arrival delayed)
0.1
1
10
100
1000
Notes: Circles on the top curve are the Erlang-C P(delay)
Squares/blocks on the bottom curve are the Erlang-B blocking prob. (not adjusted for RTA/RASTA)
All later graphs would look like these, so instead we graph % difference from Exponential (via CTMC, not simulation)

## Slide 12: What We Expected to See
% Diff from Exp.
Retrial Rate 
-100%
0%
100%?
High variability
Low variability
Notes: Expect to see this for Lo or Pd, etc.
Decays to zero for high retrial rates (acts like queue with Service In Random Order)
Decays to zero for low retrial rates (if retrial times are long, distribution won’t matter since system reaches steady-state while you’re in orbit)
Our main question was: how high is this peak? (that is, worst-case scenario)
Other questions: How quickly does the % diff decay as retrial rate increases?
As retrial rate decreases, is % diff convex, concave, linear?
Let’s look at the % difference in Lo for Deterministic retrials vs. exponential retrials.

## Slide 13: % Diff: Average Number in Orbit
Traffic = 9
Notes: Expect it to be mildly negative,
But it’s large and positive for low retrial rates
Perhaps the % error does go back to zero for retrial rates below the lowest on this graph, rr=0.1 We tried 0.01 and 0.001 and saw the % error stays at about 36% for Lo and 10% for P(delay) RetRate Lo StdErr Exp.Lo %difffromExp StdErr of % 0.001 1932.0 3.3 1414.9 36.5 9.1 0.01 194.8 0.8 142.4 36.8 2.3 RetRate pd StdErr Exp.Pd %difffromExp StdErr of % 0.001 0.149123529 0.00017 0.13581 9.8 0.0018 0.01 0.150076471 0.00042 0.13620 10.2 0.0042

## Slide 14: % Diff: Average Number in Orbit
Traffic = 16

## Slide 15: % Diff: Average Number in Orbit
Traffic = 25

## Slide 16: % Diff: Average Number in Orbit
Traffic = 36
Notes: It’s getting worse!
Let’s look at Pr(delay)

## Slide 17: % Diff: Pr(new arrival delayed)
Traffic = 9

## Slide 18: % Diff: Pr(new arrival delayed)
Traffic = 16

## Slide 19: % Diff: Pr(new arrival delayed)
Traffic = 25

## Slide 20: % Diff: Pr(new arrival delayed)
Traffic = 36

## Slide 21: WHY?

## Slide 22: Exponential Retrials
 | Retry 1 | Retry 2 | Retry 3 | Retry 4
Job 1 | 10 | 27 | 4 | 22
Job 2 | 19 | 11 | 23 | 5
Job 3 | 7 | 51 | 13 | 17
Notes: Each cell is independent of all other cells.

## Slide 23: Personal Retrial Times (PRT)
 | Retry 1 | Retry 2 | Retry 3 | Retry 4
Job 1 | 10 | 10 | 10 | 10
Job 2 | 19 | 19 | 19 | 19
Job 3 | 7 | 7 | 7 | 7
Notes: This is realistic in some cases: some devices set to retry rapidly, others slowly.

## Slide 24: Shared Sequence of Retrial Times (SSRT)
 | Retry 1 | Retry 2 | Retry 3 | Retry 4
Job 1 | 10 | 27 | 4 | 22
Job 2 | 10 | 27 | 4 | 22
Job 3 | 10 | 27 | 4 | 22

## Slide 25: Deterministic Retrials
 | Retry 1 | Retry 2 | Retry 3 | Retry 4
Job 1 | 10 | 10 | 10 | 10
Job 2 | 10 | 10 | 10 | 10
Job 3 | 10 | 10 | 10 | 10
Notes: So, deterministic retrials = both PRT and SSRT
Which is the more important effect?
Of course, there are other ways to interpolate between M and D retrials.
The most obvious: everything still IID, but non-Exponential (e.g. Gamma or Weibull)

## Slide 26: % Diff in Lo: PRT vs M

## Slide 27: % Diff in Lo: SSRT vs M
Notes: Now we see that effect at low retrial rates.
Larger errorbars: retrial rate is effectively determined by the first column in the previous table.

## Slide 28: Why? Because:
Shared Sequence of Retrial Times is the dominant effect.
How deterministic does it have to be?
We will change the Coefficient of Variation (CV)
F G
F G
F G
F G

## Slide 29: % Diff in Lo
-0.2
0
0.2
0.4
0.6
0.8
1
1.2
-5
0
5
10
15
20
25
30
Retrial Rate = 0.1
CV
% difference in Lo
Notes: We used Weibull retrial times because they are faster to simulate than Gamma/Erlangs.
Need CV of 1/10 to see the curve go positive,
Need CV of 1/100 to see strong effect.

## Slide 30: % Diff in Pr(delay)

## Slide 31: Markovian Approach
M/M/c/0 + PH2 retrials
Lower limit on variability:
  Two-phase Erlang has Squared Coefficient of Variation = 1/2
Can get lower SCV using negative(!) probabilities

## Slide 32: Extended Probabilities
1955, Cox: Complex probabilities
1987, Nojo and Watanabe:
  Negative branching Probability (NP) distrib.
1994, Graham, Knuth, Patashnik
1999, Ball et al.:
  H2* distribution
2007/8, Tijms: M/D/1 via M/PH2/1
Quantum physics
Notes: Knuth, page 403
Ball calls it the Generalized Exponential (GE) distribution; Ward Whitt calls it the H2* distribution.
We use the two highlighted distributions here.

## Slide 33: Cox-Marie distribution
Orbit 1
Orbit 2
Notes: A 2-phase Coxian distribution, with parameters determined by Marie’s formulas to match desired first and second moments.
Marie’s formulas were given in A.O. Allen’s book.

## Slide 34: Cox-Marie distribution
0
1
2
3
4
5
-100
-80
-60
-40
-20
0
20
Time
CM distribution, CV = 0.1
PDF
CDF
Notes: Cox-Marie distribution at low CV values has large entries in the PH CTMC matrix.
This causes severe ill-conditioning in the CTMC for the whole retrial queue.
Here we can see them via their effect on the PDF and CDF: the large (negative) values.

## Slide 35: NP distribution, SCV > 1/2
Orbit 1
Orbit 2
Notes: We chose to make the 3rd moment match the 3rd moment of a Gamma with the same mean and SCV.

## Slide 36: NP distribution, SCV = 1/2
Orbit 1
Orbit 2
Notes: We chose to make the 3rd moment match the 3rd moment of a Gamma with the same mean and SCV.

## Slide 37: NP distribution, SCV < 1/2
Orbit 1
Orbit 2
Notes: We chose to make the 3rd moment match the 3rd moment of a Gamma with the same mean and SCV.

## Slide 38: NP Distribution
0
1
2
3
4
5
-2
-1
0
1
Time
NP distribution, CV = 0.1
PDF
CDF
Notes: Hard to see here, but the PDF dips negative between roughly t=3 and t=4.
There seems to be a bound of -2 on how low the PDF goes.

## Slide 39: H2* distribution
∞
Orbit 1
p
1-p

## Slide 40: H2* distribution
Orbit 1
p
1-p
Notes: This allows us to essentially ignore the instantaneous retrials, and consider only how many people are in phase 1 of orbit,
Converting it to a simple exponential-retrial model with longer retrial times [slower rates] (if SCV>1) or shorter retrial times [faster rates] (if SCV<1)

## Slide 41: H2* distribution, SCV < 1
Orbit 1
p
1-p
Notes: This allows us to essentially ignore the instantaneous retrials, and consider only how many people are in phase 1 of orbit,
Converting it to a simple exponential-retrial model with longer retrial times [slower rates] (if SCV>1) or shorter retrial times [faster rates] (if SCV<1)

## Slide 42: H2* distribution
0
1
2
3
4
5
-1
0
1
2
3
4
Time
CV = 0.1
PDF
CDF
Notes: For any given mean and SCV, has the smallest possible 3rd moment among all H2 distributions.

## Slide 43: Recall our simulations: Lo
-0.2
0
0.2
0.4
0.6
0.8
1
1.2
-5
0
5
10
15
20
25
30
Retrial Rate = 0.1
CV
% difference in Lo
Notes: We used Weibull retrial times because they are faster to simulate than Gamma/Erlangs.
Need CV of 1/10 to see the curve go positive,
Need CV of 1/100 to see strong effect.

## Slide 44: NP: % Diff in Lo

## Slide 45: H2*: % Diff in Lo

## Slide 46: Recall: % Diff in Pr(delay)

## Slide 47: NP: % Diff in Pr(delay)

## Slide 48: H2*: % Diff in Pr(delay)

## Slide 49: Conclusions
Do not use exponential retrials as an approximation to G-retrials when CV < 0.1 and retrial rate <= 0.1
NP and H2* distributions do not replicate simulations at low CV

## Slide 50: Queue-and-eh?
Andrew Ross, andrew.ross@emich.edu
David Lubke, dlubke@emich.edu
Andrew Livingston, alivings@emich.edu
Katie Ballentine, knballentine@gmail.com

## Slide 51: Appendix

## Slide 52: General-Retrials literature
Yang, Posner, Templeton, Li (1994): An approximation for M/G/1+G-retrials
Many authors: only one person in orbit may retry (“constant retrial policy”)

## Slide 53: Pr(retry fails) as system grows

## Slide 54: P(retry fail)/P(new fail)

## Slide 55: % Diff: Average Number in Orbit

## Slide 56: Cox-Marie
Orbit 1
Orbit 2

## Slide 57: NP distribution
Orbit 1
Orbit 2

## Slide 58: H2* distribution
∞
Queue
Service
Orbit 1
Sys Out

## Slide 59: Very Low Retrial Rates, D-retrials
RetryRate | Lo | StdErr |  | Expon. Lo | %diff from Exp | StdErr of %
0.001 | 1931.987 | 3.332592 |  | 1414.9 | 36.54584 | 9.118938
0.01 | 194.7987 | 0.832853 |  | 142.39 | 36.80644 | 2.26279
RetryRate | P(delay) | StdErr |  | Expon. Pd | %diff from Exp | StdErr of %
0.001 | 0.149124 | 0.000172 |  | 0.13581 | 9.803055 | 0.001757
0.01 | 0.150076 | 0.000424 |  | 0.1362 | 10.1883 | 0.004161

## Slide 60: Very Low Retrial Rates, D-retrials
RetryRate | Lo | StdErr |  | Expon. Lo | %diff from Exp | StdErr of %
0.001 | 1932 | 3.3 |  | 1415 | 36.5 | 9.1
0.01 | 195 | 0.8 |  | 142 | 36.8 | 2.3
RetryRate | P(delay) | StdErr |  | Expon. Pd | %diff from Exp | StdErr of %
0.001 | 0.1491 | 0.0001 |  | 0.1358 | 9.8 | 0.002
0.01 | 0.1500 | 0.0004 |  | 0.1362 | 10.1 | 0.004